## Slide 1: Accelerator Magnets
Luca Bottura
CERN Division LHC, CH-1211 Geneva 23, Switzerland
Luca.Bottura@cern.ch

## Slide 2: What you will learn today
SC accelerator magnet design
    Complex field representation in 2-D
    Multipoles and symmetries
    Elements of magnetic design
SC accelerator magnet construction
    Coil winding and assembly, structures
    LHC dipole
Field errors in SC accelerator magnets
    Linear and non linear contributions
    SC cable magnetization effects
    Interaction with current distribution

## Slide 3: Accelerators
What for ?
    a microscope for nuclear physics
    X-ray source (lithography, spectrography, …)
    cancer therapy
    isotopes transmutation
Operation modes
    fixed target
    collider

## Slide 4: Evolution
Livingston plot: particle energy in laboratory frame vs. commissioning year
    steady increase
    main jumps happen through technology development

## Slide 5: Why high energy ?
Shorter wavelength
    Increase resolution
Higher mass
    New particles
Explore early universe time, corresponding to high energy states

## Slide 6: Linear accelerators
Sequence of
    accelerating stations (cavities), and
    focussing elements (quadrupoles)
    E and C proportional to length
accelerated
beam

## Slide 7: Circular accelerators
Sequence of
    accelerating stations (cavities),
    bending and focussing elements (magnets)

## Slide 8: Energy limits
Bending radius:
    Example : a 1 TeV (E=1000 GeV) proton (q=1) is bent by a 5 T field on a radius  = 667 m
Synchrotron radiation:
    Example : a proton (m = 1840) with 1 TeV (E=1000 GeV) bent on  = 667 m, looses E = 0.012 keV per turn

## Slide 9: Cost considerations
Total cost:
    C1 – civil engineering, proportional to length
    C2 – magnetic system, proportional to length and field strength
    C3 – installed power, proportional to the energy loss per turn

## Slide 10: CERN accelerator complex

## Slide 11: Accelerator operation
energy ramp
preparation and access
beam dump
injection phase
injection
pre-injection
I  t2
I  et
I  t
coast
coast

## Slide 12: Bending
Uniform field (dipole)
ideal
real

## Slide 13: Focussing
Gradient field (quadrupole)
focussing
de-focussing

## Slide 14: FODO cell
Sequence of:
    focussing (F) – bending (O) – defocussing (D) – bending (O) magnets
    additional correctors (see LHC example)
MB_ lattice dipole MQ lattice quadrupole
MSCB lattice sextupole+orbit corrector MO lattice octupole
MQT trim quadrupole MQS skew trim quadrupole
MCDO spool-piece decapole-octupole MCS spool-piece sextupole

## Slide 15: Magnetic field
2-D field (slender magnet), with components only in x and y and no component along z
    Ignore z and define the complex plane s = x + i y
Complex field function:
B is analytic in s
    Cauchy-Riemann conditions:

## Slide 16: Field expansion
B is analytic and can be expanded in Taylor series (the series converges) inside a current-free disk
    Magnetic field expansion:
    Multipole coefficients:

## Slide 17: Multipole magnets
B1
A1
B2
A2

## Slide 18: Normalised coefficients
Cn : absolute, complex multipoles, in T @ Rref
cn : relative multipoles, in units @ Rref
    High-order multipoles are generally small, 100 ppm and less of the main field

## Slide 19: Current line
Field and harmonics of a current line I located at R = x + iy
    Field:
    Multipoles:

## Slide 20: Magnetic moment
Field and harmonics of a moment m = my + mx located at R = x + iy
    Field:
    Multipoles:

## Slide 21: Effect of an iron yoke - I
Current line
    Image current:

## Slide 22: Effect of an iron yoke - m
Magnetic moment
    Image moment:

## Slide 23: Magnetic design - 1
Field of a cos(p) distribution
    Field:
    Multipoles:

## Slide 24: Magnetic design - 2
Field of intersecting circles (and ellipses)
    uniform field:

## Slide 25: Magnetic design - 3
Intersecting ellipses to generate a quadrupole
    uniform gradient:

## Slide 26: Magnetic design - 4
Approximation for the ideal dipole current distribution…
Rutherford cable

## Slide 27: Magnetic design - 5
… and for the ideal quadrupole current distribution…
Rutherford cable

## Slide 28: Magnetic design - 6
Uniform current shells
dipole quadrupole

## Slide 29: Tevatron dipole
2 current shells (layers)
pole
midplane

## Slide 30: HERA dipole
wedge
2 layers

## Slide 31: LHC dipole

## Slide 32: LHC quadrupole

## Slide 33: Winding in blocks
B
B

## Slide 34: Allowed harmonics
Technical current distribution can be considered as a series approximation:
=
+
+…
B = B1 + B3 + …

## Slide 35: Symmetries
Dipole symmetry:
    Rotate by  and change sign to the current – the dipole is the same
Quadrupole symmetry:
    Rotate by /2 and change sign to the current – the quadrupole is the same
Symmetry for a magnet of order m:
    Rotate by /m and change sign to the current – the magnet is the same

## Slide 36: Allowed multipoles
A magnet of order m can only contain the following multipoles (n, k, m integer)
n = (2 k + 1 ) m
    Dipole
      m=1, n={1,3,5,7,…}: dipole, sextupole, decapole …
    Quadrupole
      m=2, n={2,6,10,…}: quadrupole, dodecapole, 20-pole …
    Sextupole
      m=3, n={3,9,15,…}: sextupole, 18-pole …

## Slide 37: Dipole magnet principle

## Slide 38: Dipole magnet designs
4 T, 90 mm
4.7 T, 75 mm
6.8 T, 50 mm
3.4 T, 80 mm

## Slide 39: LHC dipole

## Slide 40: LHC dipole design
8.3 T, 56 mm

## Slide 41: Superconducting coil
B
B

## Slide 42: Rutherford cable
superconducting cable
SC strand
SC filament

## Slide 43: Collars
175 tons/m
85 tons/m
F

## Slide 44: Iron yoke
flux lines
gap between coil and yoke
heat exchanger
saturation control
bus-bar

## Slide 45: Coil ends
B

## Slide 46: Cryostated magnet

## Slide 47: Ideal transfer function
For linear materials (=const), no movements (R=const), no eddy currents (dB/dt=0)
Define a transfer function:
…
;
;

## Slide 48: Transfer function
geometric (linear) contribution
T = 0.713 T/kA
persistent currents
T = -0.6 mT/kA (0.1 %)
saturation
T = -6 mT/kA (1 %)

## Slide 49: Saturation of the field
saturated region
(B > 2 T)
effective iron boundary moves away from the coil: less field

## Slide 50: Normal sextupole
partial compensation of persistent currents at injection

## Slide 51: Persistent currents
B
+Jc
-Jc
MDC
Field change B
Eddy currents Jc with =  persistent
Diamagnetic moment at each filament:
MDCJc*Dfil
Jc(B,T)  MDC(B,B,T)

## Slide 52: Persistent currents
hysteresis crossing: no overshoot possible, operation of correctors !

## Slide 53: Persistent currents
a +0.1 K temperature increase gives a +0.17 units change on b3 (1.7 units/K)

## Slide 54: Coupling currents
 dB/dt
resistive contact at cross-overs Rc
Field ramp dB/dt
Eddy currents Ieddy
IeddydB/dt

## Slide 55: Coupling current effects
allowed and non-allowed multipoles !

## Slide 56: Decay and Snap-back
snap-back
decay
LHC operation cycle

## Slide 57: Decay and snap-back
Snap-back at the start of the acceleration ramp
decay during injection

## Slide 58: Decay
decay during simulated 10,000 s injection
exponential fit
i = 900 s

## Slide 59: Snap-back
snap-back fit:
b3 [1-(I-Iinj)/I]3
b3= 3.7units
I = 27A  B = 19 mT
snap-back
decay

## Slide 60: Decay and SB physics
Current distribution is not uniform in the cables
    joints
    supercurrents
    I/Ic
Current distribution changes in time , causing a variable rotating field...

## Slide 61: Decay and SB physics
… the local field change in turn affects the magnetization of the SC filaments: average M decreases (decay)
net decrease of magnetization

## Slide 62: Decay and SB physics
The magnetization state is re-established as soon as the background field is increased (snap-back)
The background field change necessary is of the same order of the internal field change in the cable
     100 A change in current imbalance
     10 mT average internal field change (vs. 5…20 mT measured)

## Slide 63: A demonstration
B
measured
computed
Copper strands
NbTi strand
Demonstration experiment
at Twente University.
Courtesy of M. Haverkamp

## Slide 64: A bit of reality…
Field quality reconstructed from measurements performed in MBP2N1
Plot of homogeneity |B(x,y)-B1|/B1 inside the aperture of the magnet:
    blue  OK (1  10-4)
    green  so, so (5  10-4)
    yellow  Houston, we have a problem (1  10-3)
    red  bye, bye (5  10-3)

## Slide 65: … the measurement

## Slide 66: Sony Playstation III (or Tracking the LHC...)
coil of MBP2N1
operating current
Field homogeneity reconstructed from measurements
Rref = 17 mm